## Slide 1: The TLM 2.0 Mixed Endianness Example
James Aldis
Texas Instruments France
January 2008

## Slide 2: Modification of “lt” Example
Demonstrates the use of TLM endianness-conversion functions
Illustrates data and address modification effects of BIG- and LITTLE-endian initiators sharing a memory
Allows interactive experimentation
Interactively execute “instructions” alternately on two initiators
  one big- and one little-endian
  store data from BE and view it from LE or vice-versa
  store 32-bit data and view as 8-bit or 16-bit, etc
Notes: - typical things

## Slide 3: Platform Structure
tlm_initiator_socket
tlm_target_socket
Router (SimpleBusLT)
Memory 1
(at_target_1_phase)
BE Generator 101
(initiator_top)
LE Generator 102
(initiator_top)
Memory 2
(at_target_4_phase)
32 bit
32 bit
32 bit
32 bit
Notes: Indicate which parts are TLM 2 vs. SystemC

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/lt_mixed_endian/build-unix
make
make run (uses default input)
./lt.exe (interactive input)

## Slide 5: Component details
Generator 101
  32-bit Big-endian initiator
  stdin provides instructions to execute (loads and stores)
  stdin provides data for stores
  data from loads written to stdout
Generator 102
  Identical but Little-endian
Instruction Set for both Generators
  l8, l16, l32 (load byte, halfword or word)
  s8, s16, s32 (store byte, halfword or word)
  w (switch control to other generator)
  q (quit)
  see examples/tlm/lt_mixed_endian/results/input.txt for example instructions
Bus and Memory
  Exactly as in lt example
  Some kind of 32-bit routing and memory system

## Slide 6: The System Being Modelled
Both memories are simple arrays of 4-byte words
Neither the memories nor the interconnect is aware of the endianness of the transactions
Neither the memories nor the interconnect does any data modification:
  what the initiators put on the bus goes unchanged to the memory
Memories are endianness-neutral
  provide a consistent memory image to BE and to LE initiators
  “What I write, I read back the same”
  there are no attributes on the hardware bus except those shown opposite
32-bit Memory
Component
1024 Words / 4 kByte
10-bit
address
n_we
32-bit
data in
32-bit
data out
n_ce
4-bit byte
enable

## Slide 7: The System Being Modelled
“What the other writes, I may read back at a different address”
Example 1: single byte access
  BE initiator writes byte A5 to address 66 = 64 + 2
    see opposite for hardware bus signals
  LE initiator will find it at address 65 = 64 + 1
    see opposite for hardware bus signals
0 0 1 0
xx xx A5 xx
0 00 10
byte enable
data in
address
bit index: 8 4 0 24 16 8 0 3 0
0 0 1 0
xx xx A5 xx
0 00 10
byte enable
data out
address
bit index: 8 4 0 24 16 8 0 3 0
Address bus takes the index of the correct 32-bit word (66/4 = 16).
Fractional part of the address (2) used inside initiator to select a byte lane according to big-endian convention (more significant bits are at lower addresses)
Little-endian convention is that more significant bits are at higher addresses. To get the same data, fractional part of the address is 1

## Slide 8: The System Being Modelled
“What the other writes, I may read back at a different address”
Same effect for aligned 16-bit or 32-bit data
  But no address change for 32-bit
Example 2: 32-bit integer access
  BE initiator writes 32-bit integer 04030201 to address 256
    see opposite for hardware bus signals
  LE initiator will find the same data at the same address
    see opposite for hardware bus signals
1 1 1 1
04 03 02 01
0 00 40
byte enable
data in
address
bit index: 8 4 0 24 16 8 0 3 0
1 1 1 1
04 03 02 01
0 00 40
byte enable
data out
address
bit index: 8 4 0 24 16 8 0 3 0
Address bus takes the index of the correct 32-bit word (256/4 = 64).
Big-endian convention is that more significant bits of the integer are at lower addresses, which are at more significant bits of the bus data word.
Little-endian convention is that more significant bits of the integer are at higher addresses, which are at more significant bits of the bus data word.
Therefore it is the same as big-endian!

## Slide 9: The System Being Modelled
“What the other writes, I may read back distorted”
Example 3: write 4 consecutive bytes and read back as an integer
  BE initiator writes bytes 04, 03, 02, 01 to addresses 0, 1, 2, 3
    see opposite for hardware bus signals
  Both initiators will read the integer 04030201 at address 0
  LE initiator writes bytes 04, 03, 02, 01 to addresses 0, 1, 2, 3
    see opposite for hardware bus signals
  Both initiators will read the integer 01020304 at address 0
1 1 1 1
04 03 02 01
0 00 00
byte enable
data in
address
bit index: 8 4 0 24 16 8 0 3 0
1 1 1 1
01 02 03 04
0 00 00
byte enable
data in
address
bit index: 8 4 0 24 16 8 0 3 0
Big-endian convention is that more significant bits of the data bus word are lower addresses.
Little-endian convention is that more significant bits of the data bus word are higher addresses.

## Slide 10: The TLM Model of the System
The TLM model correctly models the above data and address distortions and all other possible ones
  In particular it gets hairy for non-address-aligned transactions
The address, data array and byte enable array in the transaction payload object are
  identical to the internal opcode of the initiator
    if the initiator endianness matches the host CPU endianness
  modified
    if the initiator endianness is different from the host CPU’s
The internal data storage of the memory models
  is not visible (we are not using DMI in this example)
  But could be a simple memcpy() between the data array in the transaction payload object and an array of unsigned char in the memory model
Therefore we can say that
  the TLM 2.0 interfaces are always “host-endian”
Model is functionally identical on BE and LE host CPUs
  but internal structure (length, address, byte enables) of transaction payload objects will differ