## Slide 1: TLM 2.0 LT with Mandatory Extension System Example
Jack Donovan, Anna Keist, Charles Wilson
ESLX, Inc.
June 2008
Notes: <number>

## Slide 2: LT with Mandatory Extension Example
The Goal is to Illustrate:
  Application of TLM 2.0 in a real system
  Use of a mandatory extension
Possible Applications:
  Architectural exploration
  Early software development
Notes: <number>
- typical things

## Slide 3: Example Block Diagram
TLM 2 GP with mandatory extension
Target Module
Initiator Module
Initiator ID
Extension
Generic Payload
This extension carries a string containing the initiators ‘ID’
Notes: <number>
- aux processor is TBD

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/lt_extension_mandatory/build-unix
make clean
make
make run

## Slide 5: How to run this example (MSVC)
Open a explorer window on examples/tlm/lt_extension_mandatory/build-windows
Launch lt_extension_mandatory.sln
Select ‘Property Manager’ from the ‘View’ menu
Under ‘lt_extension_mandatory > Debug | Win32’ select ‘systemc’
Select ‘Properties’ from the ‘View’ menu
Select ‘User Macros’ under ‘Common Properties’
Update the ‘SYSTEMC’ and ‘TLM’ entries and apply
Build and run

## Slide 6: Expected Output (expected.log)
. . .
Info: lt_initiator_extension_mandatory.cpp: 275 ns - invalidate_direct_mem_ptr
Received invalidate request - valid request
Info: lt_initiator_extension_mandatory.cpp: 350 ns - log_end
Received TLM_OK_RESPONSE, Data: 0x00000002
Info: lt_initiator_extension_mandatory.cpp: 350 ns - log_start
Creating read transaction - Addr: 0x000000000000000C
Info: lt_target_extension_mandatory.cpp: 350 ns - nb_transport_fw
Extension present, Data: generic ID
Info: lt_target_extension_mandatory.cpp: 350 ns - nb_transport_fw
Read request - Addr: 0x000000000000000C
Info: lt_initiator_extension_mandatory.cpp: 450 ns - log_end
Received TLM_OK_RESPONSE, Data: 0x00000003
Info: lt_target_extension_mandatory.cpp: 450 ns - get_dmi_ptr
Extension present, Data: generic ID
. . .
Initiator ID: 101

## Slide 7: Initiator Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Initiator Module (lt_initiator_extension_mandatory)
initiator_thread
b_transport
simple_initiator_socket
extension data
populated here
socket is bound against the extension making it mandatory

## Slide 8: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (lt_target_extension_mandatory)
b_transport
memory
memory_socket
(simple_target_socket)
extension data extracted here
socket is bound against the extension making it mandatory

## Slide 9: Expected Timing
b_transport(GP, delay)
lt_initiator
lt_target
or
at_1_phase_target