## Slide 1: TLM 2.0 Approximately Timed (AT) System Example - 2 Timing Points
Jack Donovan, Anna Keist, Charles Wilson
ESLX, Inc.
June 2008
Notes: <number>

## Slide 2: AT System Example - Annotated Timing
The Goal is to Illustrate:
  Application of TLM 2.0 in a real system
  Non-blocking (NB) option of the approximately timed style
    NB annotated timing has been referred to as "2 phase"
    Medium complexity version of non-blocking/AT
Possible Applications:
  Architectural exploration
  Early software development
  Crude Architectural Verification
Notes: <number>
- typical things

## Slide 3: Example Block Diagram
TLM 2 GP
at_target_2_phase
(m_at_target_2_phase_1)
SimpleBusAT (m_bus)
initiator_top
(m_initiator_1)
initiator_top
(m_initiator_2)
at_target_2_phase
(m_at_target_2_phase_2)
Notes: <number>
- aux processor is TBD

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/at_2_phase/build-unix
make clean
make
make run

## Slide 5: How to run this example (MSVC)
Open a explorer window on examples/tlm/at_2_phase/build-windows
Launch at_2_phase.sln
Select ‘Property Manager’ from the ‘View’ menu
Under ‘at_2_phase > Debug | Win32’ select ‘systemc’
Select ‘Properties’ from the ‘View’ menu
Select ‘User Macros’ under ‘Common Properties’
Update the ‘SYSTEMC’ and ‘TLM’ entries and apply
Build and run

## Slide 6: Expected Output (expected.log) 1 of 2
Info: traffic_generator.cpp: 0 s - traffic_generator_thread
Initiator: 101 Starting Traffic
…
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 101 starting new transaction for Addr:0x00000100
Initiator: 101 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 101 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 101 transaction waiting end-request on backward-path
…
Info: at_target_2_phase.cpp: 0 s - nb_transport_fw
Target: 201 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Target: 201 transaction moved to send-response PEQ
Target: 201 UPDATED (GP, END_REQ, 10 ns)
Info: select_initiator.cpp: 10 ns - nb_transport_bw
Initiator: 101 nb_transport_bw (GP, END_REQ, 0 s)from Addr:0x00000100
Initiator: 101 transaction waiting begin-response on backward path
Initiator: 101 ACCEPTED (GP, END_REQ, 0 s)
Info: at_target_2_phase.cpp: 10 ns - nb_transport_fw
Target: 201 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Target: 201 transaction moved to send-response PEQ
Target: 201 UPDATED (GP, END_REQ, 10 ns)

## Slide 7: Expected Output (expected.log) 2 of 2
…
Info: at_target_2_phase.cpp: 40 ns - begin_response_method
Target: 201 starting response method
Info: memory.cpp: 40 ns - print
ID: 201 COMMAND: WRITE Length: 04
Addr: 0x0000000000000100 Data: 0x00000100
Info: at_target_2_phase.cpp: 40 ns - begin_response_method
Target: 201 nb_transport_bw (GP, BEGIN_RESP, SC_ZERO_TIME)
Info: at_target_2_phase.cpp: 40 ns - begin_response_method
Target: 201 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 40 ns - nb_transport_bw
Initiator: 101 nb_transport_bw (GP, BEGIN_RESP, 0 s)from Addr:0x00000100
Initiator: 101 transaction moved to send-end-response PEQ
Initiator: 101 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 47 ns - send_end_rsp_method
Initiator: 101 starting send-end-response method
Initiator: 101 nb_transport_fw (GP, END_RESP, 0 s)
Info: select_initiator.cpp: 47 ns - send_end_rsp_method
Initiator: 101 COMPLETED (GP, END_RESP, 0 s)

## Slide 8: Initiator Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Initiator Module (initiator_top)
TLM Interface Module
(select_initiator)
Traffic Generator Module
(traffic_generator)
Request Queue
(sc_fifo)
Response Queue
(sc_fifo)
top_initiator_socket
Notes: <number>
Indicate which parts are TLM 2 vs. SystemC

## Slide 9: TLM Interface Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
TLM Interface Module (select_initiator)
nb_transport_bw
send_end_rsp_method
send_end_rsp_PEQ
initiator_thread
waiting_bw_path_map
enable_next_request_event
nb_transport_fw
nb_transport_fw
request_in_port
response_out_port
Initiator_socket

## Slide 10: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (at_2_phase_target)
nb_transport_fw
begin_response_method
memory
m_response_PEQ
memory_socket
nb_transport_bw
end_resp_rcvd_event

## Slide 11: Router Component
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Router Model (SimpleBusAT<2,2>)
target sockets (2)
initiator sockets (2)

## Slide 12: Expected Timing
nb_transport_fw(GP, END_RESP, SC_ZERO_TIME)
TLM_ACCEPTED (GP, X, T1)
nb_transport_bw(GP, BEGIN_RESP, SC_ZERO_TIME)
TLM_ACCEPTED (GP, X, T3)
……………..
select_initiator
(enable_targeting_tracking=true)
SimpleBusAT
nb_transport_fw(GP, BEGIN_REQ, SC_ZERO_TIME)
TLM_UPDATED (GP, END_REQ, T1)
nb_transport_bw(GP, BEGIN_RESP, SC_ZERO_TIME)
TLM_ACCEPTED (GP, X, SC_ZERO_TIME)
SimpleBusAT
at_2_phase
……………..
nb_transport_bw(GP, END_REQ, SC_ZERO_TIME)
TLM_ACCEPTED (GP, X, T2)
……………..
TLM_COMPLETED (GP, X, T4)
……………..
nb_transport_fw(GP, BEGIN_REQ, SC_ZERO_TIME)
nb_transport_fw(GP, END_RESP, SC_ZERO_TIME)
TLM_COMPLETED (GP, X, SC_ZERO_TIME)
……………..