## Slide 1: TLM 2.0 AT with Optional Extension System Example
Jack Donovan, Anna Keist, Charles Wilson
ESLX, Inc.
June 2008
Notes: <number>

## Slide 2: AT with Optional Extension Example
The Goal is to Illustrate:
  Application of TLM 2.0 in a real system
  Use of an optional extension
  Option of the non-blocking style
    This style has been previously referred to as "4 phase"
    Most complex version of non-blocking/AT style
Possible Applications:
  Architectural Verification
  Software Verification
  Early Performance Validation
Notes: <number>
- typical things

## Slide 3: Example Block Diagram
TLM 2 GP
Target Module
(m_at_target_4_phase_1)
Router (SimpleBusAT)
Initiator Module
(m_initiator_1)
Initiator Module
(m_initiator_2)
Target Module
(m_at_target_2_phase_2)
Initiator ID
Extension
Generic Payload
This extension carries a string containing the initiators ‘ID’
This target does not support the “optional extension”
Extension enabled in initiators and m_at_target_4_phase_1 via compiler directives, not used by m_at_target_2_phase_2
Notes: <number>
- aux processor is TBD

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/at_extension_optional/build-unix
make clean
make
make run

## Slide 5: How to run this example (MSVC)
Open a explorer window on examples/tlm/at_extension_optional/build-windows
Launch at_extension_optional.sln
Select ‘Property Manager’ from the ‘View’ menu
Under ‘at_extension_optional > Debug | Win32’ select ‘systemc’
Select ‘Properties’ from the ‘View’ menu
Select ‘User Macros’ under ‘Common Properties’
Update the ‘SYSTEMC’ and ‘TLM’ entries and apply
Build and run

## Slide 6: Expected Output (expected.log)
Initiator ID: 101
Printed from
At_target_4_phase
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 102 starting new transaction for Addr:0x00000200
Initiator: 102 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 102 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 102 transaction waiting end-request on backward-path
Info: at_target_4_phase.cpp: 0 s - nb_transport_fw
Target: 201 extension data: 'Initiator ID: 101
…
Info: at_target_4_phase.cpp: 10 ns - end_request_method
Target: 201 starting end-request method
Target: 201 transaction moved to send-response PEQ
Target: 201 nb_transport_bw (GP, END_REQ, 0 s)
Info: at_target_4_phase.cpp: 10 ns - end_request_method
Target: 201 ACCEPTED (GP, END_REQ, 0 s)
…
Info: select_initiator.cpp: 1824 ns - initiator_thread
Initiator: 101 starting new transaction for Addr:0x10000100
Initiator: 101 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 1824 ns - initiator_thread
Initiator: 101 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 101 transaction waiting end-request on backward-path
Info: at_target_2_phase.cpp: 1824 ns - nb_transport_fw
…
Initiator ID not printed from at_target_2_phase_2

## Slide 7: Initiator Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Initiator Module (initiator_top)
TLM Interface Module
(select_initiator)
Traffic Generator Module
(traffic_generator)
Request Queue
(sc_fifo)
Response Queue
(sc_fifo)
top_initiator_socket
extension data
populated here
Notes: <number>
Indicate which parts are TLM 2 vs. SystemC

## Slide 8: TLM Interface Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
TLM Interface Module (select_initiator)
nb_transport_bw
send_end_rsp_method
send_end_rsp_PEQ
initiator_thread
waiting_bw_path_map
enable_next_request_event
nb_transport_fw
nb_transport_fw
request_in_port
response_out_port
Initiator_socket

## Slide 9: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (at_4_phase_target)
nb_transport_fw
begin_response_method
memory
response_PEQ
memory_socket
nb_transport_bw
end_request_method
end_request_PEQ
end_resp_rcvd_event
extension data extracted here

## Slide 10: Router Component
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Router Model (SimpleBusAT<2,2>)
target sockets (2)
initiator sockets (2)