## Slide 1: TLM 2.0 Loosely Timed (LT) System Example - Temporal Decoupled
Jack Donovan, Anna Keist, Charles Wilson
ESLX, Inc.
June 2008
Notes: <number>

## Slide 2: AT System Example - Annotated Timing
The Goal is to Illustrate:
  Application of TLM 2.0 in a real system
  Annotated non-blocking (NB) option of the non-blocking style
    NB annotated timing has been referred to as "1 phase"
    Simplest version of non-blocking/AT
Possible Applications:
  Architectural exploration
  Early software development
Notes: <number>
- typical things

## Slide 3: Example Block Diagram
TLM 2 GP
Target Module
(lt_synch_target)
Router (SimpleBusLT)
Initiator Module
(td_initiator_top)
Initiator Module
(initiator_top)
Target Module
(lt_target)
Notes: <number>
- aux processor is TBD

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/lt_temporal_decouple/build-unix
make clean
make
make run

## Slide 5: How to run this example (MSVC)
Open a explorer window on examples/tlm/lt_temporal_decouple/build-windows
Launch lt.sln
Select ‘Property Manager’ from the ‘View’ menu
Under ‘lt_temporal_decouple > Debug | Win32’ select ‘systemc’
Select ‘Properties’ from the ‘View’ menu
Select ‘User Macros’ under ‘Common Properties’
Update the ‘SYSTEMC’ and ‘TLM’ entries and apply
Build and run

## Slide 6: Expected Output (expected.log)
....
Info: lt_initiator.cpp: 0 s - initiator_thread
Initiator: 102 b_transport(GP, 0 s)
Info: memory.cpp: 0 s - print
ID: 201 COMMAND: WRITE Length: 04
Addr: 0x0000000000000000 Data: 0x00000000
Info: lt_synch_target.cpp: 0 s - custom_b_transport
Target: 201 Forcing a synch in a temporal decoupled initiator with wait( 80 ns),
Info: lt_synch_target.cpp: 80 ns - custom_b_transport
Target: 201 return from wait will return a delay of 0 s
....
Info: lt_initiator.cpp: 80 ns - initiator_thread
Initiator: 102 b_transport returned delay = 0 s

## Slide 7: Initiator Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Initiator Modules (initiator_top or td_initiator_top)
TLM Interface Module
(lt_initiator or lt_td_initiator)
Traffic Generator Module
(traffic_generator)
Request Queue
(sc_fifo)
Response Queue
(sc_fifo)
top_initiator_socket
Notes: <number>
Indicate which parts are TLM 2 vs. SystemC

## Slide 8: TLM Interface Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
TLM Interface Module (lt_td_initiator)
initiator_thread
b_transport
request_in_port
response_out_port
simple_initiator_socket
quantum_keeper

## Slide 9: Target Module (lt_target or lt_synch_target)
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (lt_target or lt_synch_target)
b_transport
memory
memory_socket
(simple_target_socket)
lt_target and lt synch_target are
identical except lt_synch_target
calls SystemC's "wait" each time
causing the quantum_keeper to
"synch" during the next check in the
initiator

## Slide 10: Router Component
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Router Model (SimpleBusLT<2,2>)
target sockets (2)
initiator sockets (2)