## Slide 1: TLM 2.0Approximately Time (AT) System Example – Mixed AT System
Jack Donovan, Anna Keist, Charles Wilson
ESLX, Inc.
June 2008
Notes: <number>

## Slide 2: AT System Example - Annotated Timing
The Goal is to Illustrate:
  Application of TLM 2.0 in a real system
  Illustrate interoperability of different AT styles
Possible Applications:
  Architectural exploration
  Early software development
  Continued modeling with available models
Notes: <number>
- typical things

## Slide 3: Example Block Diagram
TLM 2 GP
at_target_1_phase
(m_at_target_1_phase_1)
SimpleBusAT (m_bus)
initiator_top
(m_initiator_1)
initiator_top
(m_initiator_2)
at_target_2_phase
(m_at_target_2_phase_1)
at_target_4_phase
(m_at_target_4_phase_1)
Notes: <number>
- aux processor is TBD

## Slide 4: How to run this example (Linux)
Set SYSTEMC_HOME and TLM_HOME
cd examples/tlm/at_1_phase/build-unix
make clean
make
make run

## Slide 5: How to run this example (MSVC)
Open a explorer window on examples/tlm/at_1_phase/build-windows
Launch at_1_phase.sln
Select ‘Property Manager’ from the ‘View’ menu
Under ‘at_1_phase > Debug | Win32’ select ‘systemc’
Select ‘Properties’ from the ‘View’ menu
Select ‘User Macros’ under ‘Common Properties’
Update the ‘SYSTEMC’ and ‘TLM’ entries and apply
Build and run

## Slide 6: Expected Output – Target ID: 201
Info: traffic_generator.cpp: 0 s - traffic_generator_thread
Initiator: 101 Starting Traffic
…
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 101 starting new transaction for Addr:0x00000100
Initiator: 101 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 101 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 101 transaction waiting end-request on backward-path
…
Info: at_target_1_phase.cpp: 0 s - nb_transport_fw
Target: 201 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: memory.cpp: 0 s - print
ID: 201 COMMAND: WRITE Length: 04
Addr: 0x0000000000000100 Data: 0x00000100
Info: at_target_1_phase.cpp: 0 s - nb_transport_fw
Target: 201 COMPLETED (GP, BEGIN_REQ, 40 ns)
Info: select_initiator.cpp: 40 ns - nb_transport_bw
Initiator: 101 nb_transport_bw (GP, BEGIN_RESP, 0 s)from Addr:0x00000100
Initiator: 101 target omitted end-request timing-point returning ACCEPTED

## Slide 7: Expected Output – Target ID: 202
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 102 starting new transaction for Addr:0x10000200
Initiator: 102 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 0 s - initiator_thread
Initiator: 102 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 102 transaction waiting end-request on backward-path
…
Info: select_initiator.cpp: 50 ns - nb_transport_bw
Initiator: 102 nb_transport_bw (GP, END_REQ, 0 s)from Addr:0x00000200
Initiator: 102 transaction waiting begin-response on backward path
Initiator: 102 ACCEPTED (GP, END_REQ, 0 s)
…
Info: at_target_2_phase.cpp: 80 ns - begin_response_method
Target: 202 starting response method
Info: memory.cpp: 80 ns - print
ID: 202 COMMAND: WRITE Length: 04
Addr: 0x0000000000000200 Data: 0x10000200
Info: at_target_2_phase.cpp: 80 ns - begin_response_method
Target: 202 nb_transport_bw (GP, BEGIN_RESP, SC_ZERO_TIME)
Info: at_target_2_phase.cpp: 80 ns - begin_response_method
Target: 202 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 80 ns - nb_transport_bw
Initiator: 102 nb_transport_bw (GP, BEGIN_RESP, 0 s)from Addr:0x00000200
Initiator: 102 transaction moved to send-end-response PEQ
Initiator: 102 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 87 ns - send_end_rsp_method
Initiator: 102 starting send-end-response method
Initiator: 102 nb_transport_fw (GP, END_RESP, 0 s)
Info: select_initiator.cpp: 87 ns - send_end_rsp_method
Initiator: 102 COMPLETED (GP, END_RESP, 0 s)

## Slide 8: Expected Output – Target ID: 203 (1 of 2)
Info: select_initiator.cpp: 1974 ns - initiator_thread
Initiator: 102 starting new transaction for Addr:0x20000200
Initiator: 102 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Info: select_initiator.cpp: 1974 ns - initiator_thread
Initiator: 102 ACCEPTED (GP, BEGIN_REQ, 0 s)
Initiator: 102 transaction waiting end-request on backward-path
Info: at_target_4_phase.cpp: 1974 ns - nb_transport_fw
Target: 203 nb_transport_fw (GP, BEGIN_REQ, 0 s)
Target: 203 ACCEPTED (GP, BEGIN_REQ, 0 s)
Info: at_target_4_phase.cpp: 1984 ns - end_request_method
Target: 203 starting end-request method
Target: 203 transaction moved to send-response PEQ
Target: 203 nb_transport_bw (GP, END_REQ, 0 s)
Info: at_target_4_phase.cpp: 1984 ns - end_request_method
Target: 203 ACCEPTED (GP, END_REQ, 0 s)
Info: select_initiator.cpp: 1984 ns - nb_transport_bw
Initiator: 102 nb_transport_bw (GP, END_REQ, 0 s)from Addr:0x00000200
Initiator: 102 transaction waiting begin-response on backward path
Initiator: 102 ACCEPTED (GP, END_REQ, 0 s)
…
Address modified by router!

## Slide 9: Expected Output – Target ID: 203 (2 of 2)
…
Info: at_target_4_phase.cpp: 2014 ns - begin_response_method
Target: 203 starting response method
Info: memory.cpp: 2014 ns - print
ID: 203 COMMAND: WRITE Length: 04
Addr: 0x0000000000000200 Data: 0xDFFFFDFF
Info: at_target_4_phase.cpp: 2014 ns - begin_response_method
Target: 203 nb_transport_bw (GP, BEGIN_RESP, SC_ZERO_TIME)
Info: at_target_4_phase.cpp: 2014 ns - begin_response_method
Target: 203 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 2014 ns - nb_transport_bw
Initiator: 102 nb_transport_bw (GP, BEGIN_RESP, 0 s)from Addr:0x00000200
Initiator: 102 transaction moved to send-end-response PEQ
Initiator: 102 ACCEPTED (GP, BEGIN_RESP, 0 s)
Info: select_initiator.cpp: 2021 ns - send_end_rsp_method
Initiator: 102 starting send-end-response method
Initiator: 102 nb_transport_fw (GP, END_RESP, 0 s)
Info: select_initiator.cpp: 2021 ns - send_end_rsp_method
Initiator: 102 COMPLETED (GP, END_RESP, 0 s

## Slide 10: Initiator Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Initiator Module (initiator_top)
TLM Interface Module
(select_initiator)
Traffic Generator Module
(traffic_generator)
Request Queue
(sc_fifo)
Response Queue
(sc_fifo)
top_initiator_socket
Notes: <number>
Indicate which parts are TLM 2 vs. SystemC

## Slide 11: TLM Interface Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
TLM Interface Module (select_initiator)
nb_transport_bw
send_end_rsp_method
send_end_rsp_PEQ
initiator_thread
waiting_bw_path_map
enable_next_request_event
nb_transport_bw
nb_transport_bw
request_in_port
response_out_port
Initiator_socket

## Slide 12: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (at_1_phase_target)
nb_transport_fw
begin_response_method
memory
m_response_PEQ
memory_socket
nb_transport_fw

## Slide 13: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (at_2_phase_target)
nb_transport_fw
begin_response_method
memory
m_response_PEQ
memory_socket
nb_transport_bw
end_resp_rcvd_event

## Slide 14: Target Module
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Target Module (at_4_phase_target)
nb_transport_fw
begin_response_method
memory
response_PEQ
memory_socket
nb_transport_bw
end_request_method
end_request_PEQ
end_resp_rcvd_event

## Slide 15: Router Component
tlm_initiator_socket
tlm_target_socket
sc_port
sc_export
Router Model (SimpleBusAT<2,3>)
target sockets (3)
initiator sockets (2)